## Slide 1: Printed Electronics
SolidState Technology. Progress in Printed Electronics: An Interview with PARC’s Janos Veres. 2012
Alec Roelke, Tom Tracy II
ECE 6332
Fall 2012
Notes: Alec

## Slide 2: Why Printed Electronics?
Can be printed with an inkjet printer
Use organic materials instead of silicon
Many different substrates (flexible)
Much cheaper than silicon process
Much faster to prototype
Applications
  Wearable electronics
  Flexible antennas/displays
  Materials/Electronics printing hybrid
Notes: Alec

## Slide 3: Design Flow
Update Design Kit
Add Layers
Add Devices
Design Rules
Model
Layout
Layout to Bitmap
Schematic
DRC
LVS
Simulation
Manual
Layout to Bitmap
Layout to Bitmap
Print
Print
Print
Notes: Tom
- First update the design kit; design rules will be affected by applications and may become part of the design flow
- The rest of the design flow mimics the current silicon flow, with the exception of the last two steps.
Each printer has its own input format and might not have GDSII conversion support
*The process of updating the design kit is all manual! (prone to mistakes, difficult, slower, etc)

## Slide 4: Problem Statement
Printed electronics still lacks a standardized design flow. There are several competing printer manufacturers selling design kits and materials that are meant to only be used with their hardware. This makes collaboration and experimental replication difficult.
Solution Statement
Develop a configurable design flow for the design, simulation, verification, and printing of printed electronics that is meant to work with all printing materials and printers.
Notes: Tom

## Slide 5: OPDK: Organic Process Design Kit
Created by University of Minnesota's Wei Zhang, Ph.D
Design of printable Organic Thin Film Transistors (OTFTs)
Devices
  PTFT_P3HT_TG: Top-Gated P-type OTFT
  TFT_CNT_TG: Top-Gated Pass TFT
  Resistor
  Capacitor
W. Zhang. University of Minnesota VLSI Group. The Organic Process Design Kit (OPDK). 2011
N-Type TFT? :(
Notes: Tom

## Slide 6: Developing a Configurable Design Flow
Add new materials
Add new devices
Add design rules
Conversion to printable format
Notes: Tom

## Slide 7: Adding New Materials
Materials are represented as layers in Cadence
Layers are stored in the techfile
Use DEFT to edit the OPDK techfile
  Add layer name, display properties, priority
Notes: Tom
- Added n-type semiconductor layer
- Used an existing Cadence Design tool to add new layers, and display properties

## Slide 8: Adding New Devices
Devices are stored in databases by Cadence
The databases contain information about:
  sizes
  associated layers
  parameters (for PCell)
  model
Edit LVS
Notes: Tom

## Slide 9: Simulation
Added n-type layer and created NTFT_BBL_TG device
Added model for device.
Created inverter schematic and simulated
Notes: Tom

## Slide 10: Adding Design Rules
Define process rules about layer arrangement
Entirely manual
Created DRC editor that parses the file and provides editor interface
Notes: Alec

## Slide 11: Layout to Bitmap
Printer manufacturers provide proprietary tools
Francesc Vila Garcia developed a Layout2Bitmap tool that converts GDSII to bitmap
Waiting on licensing
Notes: Tom

## Slide 12: Future Work
Collaborate with Garcia and TDK4PE coalition
Automate
  Layer addition
  Device creation
  Rules configuration
Notes: Alec

## Slide 13: Conclusion
Created tutorials to configure PDK
Created DRC tool to simplify editing design rules
Extended OPDK with N-type OTFT
Collaborating with international group
Notes: Alec